## Slide 1: Semantic Segmentation with Deep Learning for Microstructural Characterization and Analysis
Prepared By: Ricardo Zambrano

## Slide 2: Goal
The goal of the project is to train a model for microstructure segmentation, a common task in metallography
The system will expect a microscopy image with magnification from 50x to 1000x (can resolve features with size ≥ 0.2 micrometers)
The system should detect microstructural features in the microscopy image and return a segmentation mask as an output. This mask categorizes each pixel in an image into a class corresponding to the phase observed in the material

## Slide 3: Deviations from Initial Goals
Initially the model for this project was meant to follow the model architecture implemented by Stuckner et al in the paper “Microstructure segmentation with deep learning encoders pre-trained on a large microscopy dataset”
  The model architecture was not available
  Pretrained weights available as ‘off-the-shelf’ downloadable
  Training dataset proprietary (NASA)  Aachen-Heerlen annotated steel microstructure dataset
  Micronet Dataset: over 100,000 annotated images
  Aachen-Heerlen annotated Dataset: 1,705 annotated images

## Slide 4: Deviations from Initial Goals
Encoder – Decoder -> CNN
Encoder – Decoder -> U-Net

## Slide 5: Methodology: Metrics Intersection over union accuracy (IoU)
True Positive (TP): The area of intersection between Ground Truth (GT) and segmentation mask(S)
False Positive (FP): The predicted area outside the Ground Truth
False Negative (FN): Number of pixels in the Ground Truth area that the model failed to predict
IoU = (TP)/(TP + FN + FP)

## Slide 6: Methodology: Masks from Annotations
Reading annotated polygon
Each image would be listed more than one time in the .csv file.
An individual line represented one polygon in the image
Image Name
Polygon Center
Polygon Vertices

## Slide 7: Methodology: Masks from Annotations
Used data classes to represent the polygons and the masks

## Slide 8: Methodology: Masks from Annotations

## Slide 9: Methodology: Masks from Annotations
View of reconstructed dataset

## Slide 10: Model Training
Hyperparameters:
The model had to be trained in the cloud  Yet, not all configurations were possible: RAM, GPU Memory

## Slide 11: Model Training
Initial results (5 epochs – 100 training samples):
Idea  Use thresholding > closing > opening in Raw Mask
Ground Truth Raw Mask Processed Mask

## Slide 12: Model Training
Comparing image filters in Raw Mask
0.25
0.55

## Slide 13: Model Training

## Slide 14: Results
Overall: predicted mask > filters on raw mask

## Slide 15: Results
On the best model more than 500/850 predicted masks had IoU > .95

## Slide 16: Results: Best Predictions

## Slide 17: Results: Worst Predictions

## Slide 18: Results: ‘Subpar’ Predictions

## Slide 19: Conclusions
U-Net is a neural network architecture effective for microstructure analysis
Cases with poor IoU performance seem to be poorly annotated – This conclusion needs to be verified by an expert
False positives occurred in regions of the image that look a lot like Martensite-austenite (MA) islands
IoU performance increases with training set size and training epochs
Using image filters for post-processing raw mask was not an effective technique in the aggregate
With a larger training dataset model testing can be more thorough

## Slide 20: Thank You… Happy Summer!